## Slide 1
Digital Guitar for Reduced Pinch Strength
Opportunity: Increase the accessibility of the guitar for
individuals with reduced pinch strength (less than 70N maximum pinch strength).
Tactile Sensor
Strain Sensor
1 Piezoresistive Tactile sensor per fret, creating a 6x12 grid
Detects which fret is being held down
Requires 92% less force to fret than regular guitar
Detect tensile forces in strummed strings
Magnitude of deformation is converted into electrical resistances for mapping output volume
Low Gauge, Untuned, Nylon Strings
Objectives:
Minimize Fretting Strain
Reduce Necessary Key Pinch Strength
Maximize Number of Keys and Chords Played
Maximize Authenticity
How it Works
Which fret is pressed down
Which string is strummed
Signal mapped by algorithm
Output desired note
Required Force (N)
Required Force to Fret Guitar Per String
E
B
G
D
A
E
Digital Guitar
Acoustic Guitar
0
2
4
4
6
String Tension Per String
E
B
G
D
A
E
16
12
8
0
4
String Tension (kg)
Digital Guitar
Acoustic Guitar